The 5 five thing you need to know about arc welding.

1. Amperages: Controls heat and voltage

Amperages should be set to 100 AC

The six things that determine amperage are

1. Type of material

2. Type of rod

3. Thickness of rod

4. Thickness of material

5. Position of rod

6. Type of flux

2. Arc Gap: distance between rod and metal

The length of the arc gap should be the same size as the size of the rod

The two things that determine arc gap are:

1. Thickness of rod

2. Thichness of material

3. Angle of Rod: position at which the rod points into the metal

The angle of the rod should 90 and 20degrees.

The two things that determine angle of rod are:

- Type of weld

- Postion of weld

4. Speed: rate at which rod goes across the metal

The speed at which you should weld at is 10 sec per inch.

5. Feed: downward motion of the rod