OA set up

- Check equipment

- Make sure that set screws for both acetylene and oxygen are out

- Make sure torch gas is shut off

- Turn oxygen valve all the way on

- Turn oxygen set screw to 25 psi

- Turn acetylene valve ½ turn

- Set acetylene screw to 5 psi

- Turn torch acetylene screw ½ turn, light torch

- Turn oxygen to desired neutral flame

OA shut down

- Turn off oxygen on torch, then acetylene

- Turn off acetylene and oxygen tanks

- Bleed lines of both acetylene and oxygen tanks

- Turn set screws all the way out